## Code
Remember to clear your browser cache before downloading :)
- GUI code (Perl for quagga)
- monitor (Perl. Can be used with Asterisk, GnuGK, Cisco (you can use Cisco for CO-BGP instead of quagga), Yate. Can be easily extended.)
- monitor (TCL, can be run by Embedded Event Manager (EEM)) EEM mini-howto
- CHF code (Perl. The code implements the lookup function and the “glue” to make it work with Asterisk.) Note: You must also have the monitor script (the previous bullet) running with subroutine write_plaintext. It will populate an intermediate CO-table (at the moment a plain text file “COtable.txt”, you can easily make it use a database also). The CHF will use the intermediate table instead of the CO-BGP table directly (Option 6).
- CHF code (C. Implements the lookup function, as well as Asterisk FastAGI “bindings”.). Note: You must also have the monitor script (the previous bullet) running with subroutine write_plaintext. It will populate an intermediate CO-table (at the moment a plain text file “COtable.txt”, you can easily make it use a database also). The CHF will use the intermediate table instead of the CO-BGP table directly.
- Convert an IPv6 prefix to a telephony prefix (and vice versa; Perl)
## Configuration
### Asterisk (tested in Linux Debian 6.0)
- sip.conf
- h323.conf
- extensions.conf
- modules.conf
### GnuGK (tested in Linux Debian 6.0)
See guidelines in the comments of the monitor code (above subroutine write_gnugk).
### Yate (tested in Linux Debian 6.0)
See guidelines from the monitor code (above subroutine write_yate).
### Cisco ISR 2921
- Cisco ISR BGP configuration. NOTE: In this configuration the CO-BGP neighbor (in this example 10.10.5.12) and the “normal” eBGP neighbor (10.63.0.2) are handled from the same router. In other words, no dedicated “CO-BGP router” is needed.
- Cisco ISR voice configuration example.
### Quagga
Debian (in this example configuration, CO-BGP and the “normal” BGP are handled from the same process):
- /etc/quagga/bgpd.conf
- /etc/network/interfaces
- /etc/quagga/debian.conf
- /etc/quagga/zebra.conf
CentOS: Same as with Debian.
Note that no IPv4 networks are advertised to CO-BGP neighbor (10.10.0.12), and no IPv6 networks to CL-BGP neighbor (10.63.0.1):
# vtysh -c 'show ip bgp neighbors 10.63.0.1 advertised-routes' > 10.10.5.0/24 10.63.0.2 0 32768 i # vtysh -c 'show ipv6 bgp neighbors 10.63.0.1 advertised-routes' % No such neighbor or address family # vtysh -c 'show ip bgp neighbors 10.10.0.12 advertised-routes' # vtysh -c 'show ipv6 bgp neighbors 10.10.0.12 advertised-routes' *&gt; 2001:db8:941:215::/64 2001:db8::10:10:5:12 0 32768 i

(Scipts, configuration and documentation by Visa Holopainen -2013)